Xact Fluid Solutions

W134 N5373 Campbell Drive

Menomonee Falls, WI 53051
PH:   262-781-6500
FAX: 262-781-3906

solutions@Xactfluid.com

www.Xactfluid.com

September 1, 2004

Mr. Jim Thelen

Farmland Foods

800 Industrial Dr

Denison, IA 51442

Dear Jim:

We appreciate the opportunity to quote on your required (14) point grease lubrication system.  As specified the solution will include (14) metering pumps with ½ gallon grease reservoir capacity, 24VDC Three-Way solenoid and Low Level Sensing capability.  The system will be shipped plumbed and mounted on a back plate for ease of installation.  Solenoid valve and low level sensor are supplied with two wire leads and will require electrical connection to your existing PLC.  System is fillable via a supplied grease zirc fitting and requires air input of no less than 40psi and no more than 125psi.

System to be a positive displacement, independently adjustable, 14 point grease system.  Each lubrication point will be adjustable from 0 to .012 cubic inches of output volume per activation cycle.  Activation is recommended at no more than once every 5 seconds.  System will accept up to NLGI 2 grease at room temperature.  A ratio of 9:1 between the air supplied and the grease outlet pressure will ensure no blockages occur between the pumping system and each lubrication point.  This system has been employed in numerous other facilities since 1987 and continues to be effective, reliable and low maintenance.

Price for this system (XEAMGLS14X00005) will be: $1992.61

If you have any further questions, please feel free to contact me directly – 262-252-5670

When you call on Xact, a solution is Xactly what you will receive.

Sincerely,

Shaun M. Beauchamp


Shaun M. Beauchamp

Director of Operations